## Slide 1
Start Here
EXEMPT
No Stormwater Requirements
Figure A1. Initial Screening for All Development Projects
SFR > 2,500 ft2
See Figure A4
Is the project Exempt or does not discharge to MS4?
Project is < 2,500 ft2 of new and replaced impervious surface
Project is a detached single-family residence?
All Others
See Figure A2
YES NO
YES NO
YES NO
Flow Chart to Determine Performance Requirements

## Slide 2
Figure A2. Requirements for Small to Moderate Development Projects
Projects ≥ 2,500 ft2
Project is > 2,500 ft2 of new and replaced impervious surface but < 5,000 ft2 of net impervious area
Project is > 5,000 ft2 net impervious area but < 15,000 ft2 of new and replaced impervious surface
Project is >15,000 ft2 of new and replaced impervious surface
Performance Requirement #1 (Site Design)
Performance Requirements #1 (Site Design) and #2 (WQ Treatment)
See Figure A3

## Slide 3
Project creates > 22,500 ft2 of new and replaced impervious surface
Figure A3. Requirements for Large Development Projects
Yes
No additional Stormwater Requirements
Does the project fall under the
Special Circumstances designation?
See Special Circumstances
(Performance Requirement #5)
No
No
Watershed Management Zone
1 2 3 4 5 6 7 8 9 10
Apply Performance
Requirement #4
(Peak Management)
Projects ≥ 15,000 ft2 New and Replaced Impervious Area
Yes
Retain 95th Percentile event via infiltration
Retain 95th Percentile event via storage, harvesting, infiltration, and/or evapotranspiration
N/A
Retain 95th Percentile event via infiltration where overlying groundwater basin
Retain 85th Percentile event via infiltration
Retain 85th Percentile event via storage, harvesting, infiltration, and/or evapotranspiration
Retain 95th Percentile event via infiltration where overlying groundwater basin
Retain 85th Percentile event via infiltration
Retain 85th Percentile event via storage, harvesting, infiltration, and/or evapotranspiration
Retain 95th Percentile event via infiltration where overlying groundwater basin
Determine WMZ and apply Performance Requirement #3 (Runoff Retention)
Project in WMZ 1, 2, 3, 6, or 9
No
Yes

## Slide 4
Performance Requirement #1
Project is
> 2,500 ft2 new and replaced impervious surface,
but
< 15,000 ft2 net impervious area
Project is
> 15,000 ft2 net impervious area, but
< 22,500 ft2 new and replaced impervious surface
Performance Requirement #s
1, 2, and 3
Project is
> 22,500 ft2 new and replaced impervious surface
Performance Requirement #s
1, 2, 3, and 4
Figure A4. Requirements for Single-Family Residential Projects
Detached Single-Family Residential Projects