## Slide 1: Diversion Reporting and Measurement Regulation: Focus on the Delta
Michael Patrick George, Delta Watermaster
August 22, 2016

## Slide 2: Reporting Requirements
Includes all diverters since Delta Reform Act of 2009
Every diversion must report actual use
  Due annually, by month (currently, by June 30)
  Due more frequently during drought conditions
Statement of Diversion and Use
  STILL due, independent of new measurement requirement
  Non-filers risk loss of legal protection for the water right claim

## Slide 3: New Measurement Overview
New regulation (Jan. 19) implements SB 88
Applies to every claim to use >10 acre-feet/year
Sets measurement accuracy performance standard: ±10%
Comply with:
  Measuring device or
  Measurement method
In circumstances where standard compliance is infeasible
  Alternative compliance plan
  Specified minimum content
No regulatory approval
  Develop and implement, subject to compliance audit

## Slide 4: Measuring Devices
No “Approved Devices”
Performance standards for both accuracy and monitoring frequency
Type of Diversion (af = acre-feet) | Installation Deadline | Required accuracy | Required Monitoring Frequency | Qualifications for Installation And Certification
Direct Diversion ≥ 1,000 af/year Storage ≥ 1000 af | January 1, 2017 | 10% | Hourly | Engineer/Contractor/Professional
Direct Diversion ≥ 100 af/year Storage ≥ 200 af | July 1, 2017 | 10% | Daily | Engineer/Contractor/Professional
Direct Diversion > 10 af/year Storage ≥ 50 af | January 1, 2018 | 15% | Weekly | Individual experienced with measurement and monitoring
Storage > 10 af | January 1, 2018 | 15% | Monthly | Individual experienced with measurement and monitoring

## Slide 5: Measurement Methods
A diverter may employ a measurement method
  Must meet the same performance standard: ±10%
  Provides flexibility to adapt to individual circumstances
  Encourages cooperation among diverters on a common system
  May be simpler and more economical than meters
Examples:
  Meter at point of diversion with allocation formula to each claim
  Tidal gate with measurement algorithm tied to published tide table
  Staff gauge coupled with floodable acreage, monitoring and recording
Methods for larger diversions must be certified by a professional

## Slide 6: Measurement Methods
A diverter may employ a measurement method
  Must meet the same performance standard: ±10%
  Provides flexibility to adapt to individual circumstances
  Encourages cooperation among diverters on a common system
  May be simpler and more economical than meters
Examples:
  Meter at point of diversion with allocation formula to each claim
  Tidal gate with measurement algorithm tied to published tide table
  Staff gauge coupled with floodable acreage, monitoring and recording
Methods for larger diversions must be certified by a professional

## Slide 7: Alternative Compliance Plan
Available only where conventional compliance is not possible for a reason enumerated in the law
Requires coming as near to compliance as circumstances reasonably allow; cost is not a controlling factor
Should follow regulation check-list
To be filed and implemented; no “approval” available
Consultation, creativity and diligence are encouraged
Compliance burden remains with diverter
Plans (and progress of implementation) subject to audit, correction and, if necessary, enforcement action

## Slide 8: Specific Challenges in the Delta
Tidal influence
Use of syphons
Shared points of diversion
Fouling
Vandalism
Experimentation
Cost

## Slide 9: Extensions of Time
For good cause shown, there is authority to grant extension of time for compliance
What constitutes “good cause”?
  Demonstration of diligence, before and after
  Serious investigation of available models
  Explanation of challenges encountered
  Proposed solution strategy, with milestones
  Description of anticipated benefits/outcomes

## Slide 10: Enforcement
Outside the Delta: Water Board Division of Water Rights
Inside the Delta/Marsh: Delta Watermaster
Significant civil fines for unlawful diversion
Failure to comply jeopardizes value of water right
Objective: compliance leading to improved administration of scarce/precious resource

## Slide 11: Questions?
Contact: Lauren Barva, (916) 319-8264 or lauren.barva@waterboards.ca.gov