## Slide 1: Conjunctive Water Management and Potential for Streamflow Increase in the Scott River Watershed
Photo: Liz Bowen
North Coast Regional Water Quality Control Board Meeting
Thomas Harter, Gus Tolley, Laura Foglia, Steve Orloff, Helen Dahlke
University of California Davis & UC Ag & Natural Resources
June 29th , 2017

## Slide 10
gaining stream

## Slide 13
gaining stream

## Slide 15
Impact from Groundwater Pumping

## Slide 16
losing stream

## Slide 17
losing stream

## Slide 19
California DWR, 2017

## Slide 20: Private Monitoring Network: Seasonal Hydrographs
Chart: Seasonal Groundwater Depth
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Winter | 8.8704 | 12.8669 | 14.5514 | 19.3241 | 20.2115 | 17.2531 | 18.9967 | 18.1607 | 21.2845 | 16.5223 | 14.2757 | 10.5226
Spring | 9.5558 | 13.0384 | 15.2646 | 18.792 | 17.0765 | 14.9123 | 16.9664 | 17.3032 | 20.4049 | 19.3214 | 13.8642 | 10.615
Summer | 13.1396 | 17.7175 | 20.1955 | 23.2277 | 20.4185 | 18.072 | 21.2426 | 23.3574 | 27.3499 | 24.3898 | 19.949
Fall | 15.7444 | 18.7954 | 20.8107 | 23.6976 | 20.7847 | 19.3209 | 21.76 | 22.9314 | 23.2378 | 23.0346 | 17.6216

## Slide 21: Delayed Impact of Pumping on Stream Depletion

## Slide 22: Managed Aquifer Recharge Near a Stream

## Slide 23: Managed Aquifer Recharge Near a Stream

## Slide 24: Managed Aquifer Recharge Near a Stream

## Slide 25: Managed Aquifer Recharge Near a Stream

## Slide 26: Managed Aquifer Recharge Near a Stream

## Slide 27: Managed Aquifer Recharge Near a Stream

## Slide 28: Managed Aquifer Recharge Near a Stream

## Slide 29: Managed Aquifer Recharge Near a Stream

## Slide 30: Managed Aquifer Recharge Near a Stream

## Slide 31: Managed Aquifer Recharge Near a Stream

## Slide 32: Managed Aquifer Recharge Near a Stream

## Slide 33: Managed Aquifer Recharge Near a Stream

## Slide 34: Managed Aquifer Recharge Near a Stream

## Slide 35: Scott River Ecohydrology
Ag Growing Season
Critical
Low Flow
Period
coho
Chinook
Stream Disconnections
Increased Water Temperatures
Juvenile coho in main stem(?)

## Slide 36: Conceptual Outline of SVIHM
Upper Watershed Model
Soil-Water Budget
Model
Groundwater-Surface-Water Model
Streamflow entering Scott Valley
(Regression model)
Recharge and pumping within the valley
(Tipping bucket model)
Detailed groundwater levels and streamflow within the valley
(MODFLOW model)

## Slide 37: Soil-Water Budget Model Calibration
Measured ET and Applied Water on 3 Scott Valley Alfalfa Fields, in/yr (2012-3013)
2012 | Fawaz | Menne | Morris
ETa | 30.8 | 28.9 | 28.7
Rain + Irrig. | 18.9 | 21.7 | 22.3
2013 | Fawaz | Menne | Finley
ETa | 32.8 | 30.4 | 35.4
Rain + Irrig. | 32.3 | 27.0 | 28.5
2014 | Fawaz | Menne | Finley
ETa | 32.9 | 28.0 | 29.1
Rain + Irrig. | 29.5 | 26.1 | 22.5
Average Rain + Irrig. = 25.4
Orloff et al. (in prep)
Simulated ET and Applied Water from Soil-Water Budget Model, in/yr (1990-2011)
Initial
Irrigation Rates Overestimated
Updated
Irrigation Rates Agree with Measured Values
Foglia et al. (2013a)
Average Rain ~5-6 in

## Slide 38: MODFLOW Model Calibration

## Slide 39: MODFLOW Model Calibration
Model results match observed head and streamflow very well

## Slide 40: MODFLOW Model Validation
Very good agreement between observed dry sections and simulated dry sections for different water year types

## Slide 41: SVIHM Applications
Learning tool
  Basin water budget
  Hydrologic flow paths and residence times
  Identify data gaps
Management tool
  Estimate current hydrologic conditions
  Predict hydrologic conditions given future climate predictions (forecasting)
Scenario testing
  “What if…”
  Not limited by legal, physical, or financial constraints (except for computational costs)
  Can provide guidance for which scenarios may be the most promising to pursue relative to each other

## Slide 42: SVIHM Applications
Learning tool
  Basin water budget
  Hydrologic flow paths and residence times
  Identify data gaps
Management tool
  Estimate current hydrologic conditions
  Predict hydrologic conditions given future climate predictions (forecasting)
Scenario testing
  “What if…”
  Not limited by legal, physical, or financial constraints (except for computational costs)
  Can provide guidance for which scenarios may be the most promising to pursue relative to each other

## Slide 43: Estimated Groundwater Storage Change
Chart: Groundwater Storage
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
 | 40385.5865 | 17968.7545 | 8519.8465 | -18250.6195 | -23228.9585 | -6635.8405 | -16416.4505 | -11727.8775 | -29249.5265 | -2539.0615 | 10061.8045 | 31112.3425

## Slide 44: SVIHM Applications
Learning tool
  Basin water budget
  Hydrologic flow paths and residence times
  Identify data gaps
Management tool
  Estimate current hydrologic conditions
  Predict hydrologic conditions given future climate predictions (forecasting)
Scenario testing
  “What if…”
  Not limited by legal, physical, or financial constraints (except for computational costs)
  Can provide guidance for which scenarios may be the most promising to pursue relative to each other

## Slide 45: Conjunctive Water Use
Scott Valley is a storage-limited system
  Average annual discharge is 5x average ET demand
  Plenty of water, just not at the right time
Increase residence time of water in the valley
  Surface water: hours to days
  Groundwater: days to months (years?)
Ag
Growing Season

## Slide 46: Conjunctive Water Use
Scott Valley is a storage-limited system
  Average annual discharge is 5x average ET demand
  Plenty of water, just not at the right time
Increase residence time of water in the valley
  Surface water: hours to days
  Groundwater: days to months (years?)
Add a hydrologic “speed bump”

## Slide 47: Conjunctive Use Scenarios
4 conjunctive use scenarios identified:
1) Managed Aquifer Recharge (MAR)
2) In Lieu Recharge (ILR)
3) Combination of MAR and ILR
4) Beaver Dams

## Slide 48: Managed Aquifer Recharge
Use agricultural fields as temporary spreading basins during winter months
  Flood fields during crop dormancy
  Flows are high and demand is low
Increase residence time of water in the valley
  Surface water: hours to days
  Groundwater: days to months
CA&ES Outlook F2015

## Slide 49: Managed Aquifer Recharge – Potential Concerns
Does this cause additional consumptive water use?
  MAR timing is during crop dormancy
  Growers are already irrigating as much as they want/can
    No agricultural expansion expected
  Additional recharge will be partitioned to:
    Increased streamflow (vast majority of MAR water)
    Increased ET from native riparian vegetation

## Slide 50: Managed Aquifer Recharge – Potential Concerns
Will this negatively affect fish habitat during the winter months?
  Winter diversion is less than 5% of average flow at that time
  Potential for habitat benefit in the summer far exceeds potential harm during the winter

## Slide 51: Managed Aquifer Recharge
Use selected fields as temporary spreading basins
  ~1,400 acres
Divert water January through March at SVID Ditch and apply to fields
  ~7,500 acre-ft
Leverages current infrastructure with lowest investment cost
  Easiest scenario to implement

## Slide 52: Managed Aquifer Recharge
Use selected fields as temporary spreading basins
  ~1,400 acres
Divert water January through March at SVID Ditch and apply to fields
  ~7,500 acre-ft total
Leverages current infrastructure with lowest investment cost
  Easiest scenario to implement

## Slide 53: Managed Aquifer Recharge
Use selected fields as temporary spreading basins
  ~1,400 acres
Divert water January through March at SVID Ditch and apply to fields
  ~7,500 acre-ft total
Leverages current infrastructure for lowest investment cost
  Easiest scenario to implement

## Slide 54: Managed Aquifer Recharge – Preliminary Results
Decreased flow due to diversion for recharge
Increased flow due to groundwater discharge to Scott River

## Slide 55: Managed Aquifer Recharge – Preliminary Results

## Slide 56: Managed Aquifer Recharge – Pilot Project
15 acre 9-yr old alfalfa stand
Stoner gravelly sandy loam
Three winter water application rates:
  Continuous – every day
  High – 3-5 water applications per week
  Low – 1-3 water applications per week
  Standard - no winter water application

## Slide 57: Managed Aquifer Recharge – Pilot Project
 | Precipitation | Applied winter water | Total annual deep percolationa | Deep percolation from winter water application | Deep percolation as percent of applied water | Contribution to soil storage b | 
 | in | in | In | in | % | in | %
SCOTT VALLEY - 2015 |  |  |  |  |  |  | 
Standard | 19.6 | 0.0 | 7.8 | - | - | - | -
Low | 19.6 | 47.2 | 51.8 | 44.0 | 93% | 3.2 | 6.8%
High | 19.6 | 87.0 | 91.4 | 83.6 | 96% | 3.4 | 3.9%
Continuous | 19.6 | 310.6 | 314.5 | 306.8 | 99% | 3.7 | 1.2%
SCOTT VALLEY - 2016 |  |  |  |  |  |  | 
Standard | 23.7 | 0.0 | 11.2 | - | - | - | -
Low | 23.7 | 19.8 | 30.9 | 19.7 | 99% | 0.2 | 0.8%
High | 23.7 | 48.5 | 59.6 | 48.7 | 100% | 0.2 | 0.3%
Continuous | 23.7 | 130.6 | 141.7 | 130.5 | 100% | 0.1 | 0.1%
Check 7 | 23.7 | 155.6 | 163.8 | 152.6 | 98% | 3.0 | 1.9%
a includes deep percolation from precipitation
b amount of applied winter water used to bring soil water content to field capacity
1 inch = 2.54 cm
3.6 ft
7. 0 ft
25.6 ft
Up to 25.6 ft/acre recharged with >90% reaching groundwater table
No discernable effect on crop yield (needs further investigation)
Dahlke et al. (in prep)

## Slide 58: In Lieu Recharge
Use surface water instead of groundwater when available on selected fields
  ~5,900 acres
Delays portion of groundwater pumping until later in the summer
  Important streamflow depletion effects

## Slide 59: In Lieu Recharge
Use surface water instead of groundwater when available on selected fields
  ~5,900 acres
Delays portion of groundwater pumping until later in the summer
  Important streamflow depletion effects

## Slide 60: In Lieu Recharge – Preliminary Results
Decreased flow due to diversion for recharge
Increased flow due to groundwater discharge to Scott River

## Slide 61: In Lieu Recharge – Preliminary Results

## Slide 62: In Lieu Recharge – Preliminary Results

## Slide 63: In Lieu Recharge– Potential Concerns
Reduction of spring and summer flows due to increased diversions
Are the negative impacts in the spring and early-summer outweighed by the late-summer benefits?
  SVIHM suggests they are
  Likely need more complex 2D surface-water modeling (velocity and depth) for more detailed quantitative assessment

## Slide 64: In Lieu Recharge– Concerns
Reduction of spring and summer flows due to increased diversions
Are the negative impacts in the spring and early-summer outweighed by the late-summer benefits?
  SVIHM suggests they are
  Likely need more complex 2D surface-water modeling (velocity and depth) for more detailed quantitative assessment
GHSI – Fish Habitat Index
Weiner, in prep
Predominantly
Flood Irrigation
With SW
Sprinkler & Flood Irrigation, GW & SW

## Slide 65: Conclusions
Conjunctive use management represents a potential win-win scenario for farmers and fish
  Streamflow increases during critically dry period (summer/fall)
  Decreased groundwater pumping while applying same amount of water to agricultural fields
Potential for synergistic benefits implementing the two scenarios simultaneously
Sari Sommarstrom

## Slide 66: Conclusions
Conjunctive use management represents a potential win-win scenario for farmers and fish
  Streamflow increases during critically dry period
  Decreased groundwater pumping while applying same amount of water to agricultural fields
Potential for synergistic benefits implementing the two scenarios simultaneously

## Slide 67: Future Work
  Incorporate model parameter uncertainty into scenario analysis
Add feedback from MODFLOW model to soil-water budget model (nearly complete)
  Currently uni-directional coupling between the two
  Add capability to model effects of beaver dams or beaver dam analogs (BDAs)
Create “pre-development” version of SVIHM
  Model natural, “unimpaired” flows in the valley
Create more sophisticated upper-watershed model
  Climate change applications
  Explore effects of forest management scenarios on valley water supplies
http://www.blendspace.com
Scott River Watershed Council
Scott River Watershed Council

## Slide 68: Future Work
  Incorporate model parameter uncertainty into scenario analysis
Add feedback from MODFLOW model to soil-water budget model
  Currently uni-directional coupling between the two
  Add capability to model effects of beaver dams or beaver dam analogs (BDAs)
Create “pre-development” version of SVIHM
  Model natural, “unimpaired” flows in the valley
Create more sophisticated upper-watershed model
  Climate change applications
  Explore effects of forest management scenarios on valley water supplies
http://www.blendspace.com
Scott River Watershed Council
Scott River Watershed Council
Soil-Water Budget
Model
Groundwater-Surface-Water Model

## Slide 69: Future Work
  Incorporate model parameter uncertainty into scenario analysis
Add feedback from MODFLOW model to soil-water budget model
  Currently uni-directional coupling between the two
  Add capability to model effects of beaver dams or beaver dam analogs (BDAs)
Create “pre-development” version of SVIHM
  Model natural, “unimpaired” flows in the valley
Create more sophisticated upper-watershed model
  Climate change applications
  Explore effects of forest management scenarios on valley water supplies
http://www.blendspace.com
Scott River Watershed Council
Scott River Watershed Council
http://www.blendspace.com
Scott River Watershed Council

## Slide 70: Future Work
  Incorporate model parameter uncertainty into scenario analysis
Add feedback from MODFLOW model to soil-water budget model
  Currently uni-directional coupling between the two
  Add capability to model effects of beaver dams or beaver dam analogs (BDAs)
Create “pre-development” version of SVIHM
  Model natural, “unimpaired” flows in the valley
Create more sophisticated upper-watershed model
  Climate change applications
  Explore effects of forest management scenarios on valley water supplies
http://www.blendspace.com
Scott River Watershed Council
Scott River Watershed Council

## Slide 71: Future Work
  Incorporate model parameter uncertainty into scenario analysis
Add feedback from MODFLOW model to soil-water budget model
  Currently uni-directional coupling between the two
  Add capability to model effects of beaver dams or beaver dam analogs (BDAs)
Create “pre-development” version of SVIHM
  Model natural, “unimpaired” flows in the valley
Create more sophisticated upper-watershed model
  Climate change applications
  Explore effects of forest management scenarios on valley water supplies
http://www.blendspace.com
Scott River Watershed Council

## Slide 72: References
Coe, J. J. (1990). Conjunctive use-advantages, constraints, and examples. Journal of irrigation and drainage engineering, 116(3), 427-443.
Foglia, L., Mcnally, A., Hall, C., Ledesma, L., Hines, R., & Harter, T. (2013). Scott Valley Integrated Hydrologic Model : Data Collection, Analysis, and Water Budget, 101 p.
Niswonger, R. G., Panday, S., & Ibaraki, M. (2011). MODFLOW-NWT, a Newton formulation for MODFLOW-2005. US Geological Survey Techniques and Methods, 6, A37
Niswonger, R. G., & Prudic, D. E. (2005). Documentation of the Streamflow-Routing (SFR2) Package to Include Unsaturated Flow Beneath Streams—A Modification to SFR1: U.S. Geological Survey Techniques and Methods 6-A13. U.S. Geological Survey, (April 2010), 59 p.
Mack, S. (1958). Geology and ground-water features of Scott Valley, Siskiyou County, California. USGS Water-supply paper 1462, 110 p.

## Slide 73
Questions?

## Slide 74: SVIHM – Average Annual Aquifer Budgets

## Slide 75: UCD and Affiliated Data Collection and Analysis
Pumping test analysis
  Physical hydraulic properties of aquifer
Evapotranspiration
  Estimated
  Surface renewal
  New CIMIS station (225)
Soil moisture and texture sampling
Applied irrigation rates
Well log digitization
Voluntary groundwater monitoring program
SAGBI

## Slide 76: UCD and Affiliated Data Collection and Analysis
Pumping test analysis
  Physical hydraulic properties of aquifer
Evapotranspiration
  Estimated
  Surface renewal
  New CIMIS station (225)
Soil moisture and texture sampling
Applied irrigation rates
Well log digitization
Voluntary groundwater monitoring program
SAGBI
Orloff, Snyder, and Harter, in preparation

## Slide 77: UCD and Affiliated Data Collection and Analysis
Pumping test analysis
  Physical hydraulic properties of aquifer
Evapotranspiration
  Estimated
  Surface renewal
  New CIMIS station (225)
Soil moisture and texture sampling
Applied irrigation rates
Well log digitization
Voluntary groundwater monitoring program
SAGBI
Orloff, Snyder, and Harter, in preparation

## Slide 78: UCD and Affiliated Data Collection and Analysis
Pumping test analysis
  Physical hydraulic properties of aquifer
Evapotranspiration
  Estimated
  Surface renewal
  New CIMIS station (225)
Soil moisture and texture sampling
Applied irrigation rates
Well log digitization
Voluntary groundwater monitoring program
SAGBI
Orloff, Snyder, and Harter, in preparation

## Slide 79: Stakeholder Involvement
UCD Team Meetings with
  Siskiyou County
  Scott Valley Groundwater Advisory Committee
  Cooperative Extension
  Community Meetings
  Resources Conservation District
  Scott River Watershed Council
  USDA Natural Resources Conservation Service
  Quartz Valley Tribe
  Karuk Tribe
  Department of Water Resources
  Department of Fish and Wildlife
  SWRCB
Field work coordinated with
  RCD
  Local landowners
  Scott Valley GWAC

## Slide 80: Managed Aquifer Recharge - Results
total simulated streamflow recovery after 13 years: > 99.5%

## Slide 81: Conjunctive Use
Conjunctive water use
  Coordinated management of surface-water and groundwater supplies to improve water availability and reliability
  Treat surface-water and groundwater as a single resource, instead of two separate resources as is commonly done
Goals
  Maintain current agricultural production in the valley
  Increase groundwater discharge to Scott River during the late-summer

## Slide 82: Conjunctive Use Methodology
Growing Season
Critical Streamflow Period
Critical Streamflow Period = Baseflow Dominant

## Slide 83: Conjunctive Use Methodology
Aquifer Water Budget

## Slide 84: Conjunctive Use Methodology
Aquifer Water Budget

## Slide 85: Conjunctive Use
Conjunctive water use
  Coordinated management of surface-water and groundwater supplies to improve water availability and reliability
  Treat surface-water and groundwater as a single resource, instead of two separate resources as is commonly done
Goals
  Maintain current agricultural production in the valley
  Increase groundwater discharge to Scott River during the late-summer

## Slide 86: Available Data
Climate station data
  Precipitation
  Temperature
  Humidity
  Wind speed
  Cloud Cover
Streamflow data
  USGS Fort Jones Gauge
  RCD Gauges
Land use data
  CADWR land use survey
Groundwater levels
  DWR
Soil Data

## Slide 87: Available Data
Climate station data
  Precipitation
  Temperature
  Humidity
  Wind speed
  Cloud Cover
Streamflow data
  USGS Fort Jones Gauge
  RCD Gauges
Land use data
  CADWR land use survey
Groundwater levels
  DWR
Soil Data
Notes: Climate and streamflow analysis by Courtney Hall, in the UC Davis 2013 report on SVIHM and in the WRR article in 2013

## Slide 88: Available Data
Climate station data
  Precipitation
  Temperature
  Humidity
  Wind speed
  Cloud Cover
Streamflow data
  USGS Fort Jones Gauge
  RCD Gauges
Land use data
  CADWR land use survey
Groundwater levels
  DWR
Soil Data

## Slide 89: Available Data
Climate station data
  Precipitation
  Temperature
  Humidity
  Wind speed
  Cloud Cover
Streamflow data
  USGS Fort Jones Gauge
  RCD Gauges
Land use data
  CADWR land use survey
Groundwater levels
  DWR
Soil Data

## Slide 90: Available Data
Climate station data
  Precipitation
  Temperature
  Humidity
  Wind speed
  Cloud Cover
Streamflow data
  USGS Fort Jones Gauge
  RCD Gauges
Land use data
  CADWR land use survey
Groundwater levels
  DWR
Soil Data

## Slide 91: Study Area
Scott Valley
  Watershed: 2,100 km2 (800 mi2)
    Valley: 200 km2 (77 mi2 = 50k ac)
  Mediterranean Climate
    Wet winters and dry summers
  “Bathtub” style sedimentary basin
    Up to 76 m (250 ft) thick aquifer
  Scott River flows from south to north
    12 major tributary streams
    2 major diversion ditches

## Slide 92: Climate
Scott Valley
  Watershed: 2,100 km2 (800 mi2)
    Valley: 200 km2 (77 mi2 = 50k ac)
  Mediterranean Climate
    Wet winters and dry summers
  “Bathtub” style sedimentary basin
    Up to 76 m (250 ft) thick aquifer
  Scott River flows from south to north
    12 major tributary streams
    2 major diversion ditches
PRISM (2013)

## Slide 93: Geology
Scott Valley
  Watershed: 2,100 km2 (800 mi2)
    Valley: 200 km2 (77 mi2 = 50k ac)
  Mediterranean Climate
    Wet winters and dry summers
  “Bathtub” style sedimentary basin
    Up to 76 m (250 ft) thick aquifer
  Scott River flows from south to north
    12 major tributary streams
    2 major diversion ditches
D’
D
D
D’
Mack (1958)

## Slide 94: Hydrology
Scott Valley
  Watershed: 2,100 km2 (800 mi2)
    Valley: 200 km2 (77 mi2 = 50k ac)
  Mediterranean Climate
    Wet winters and dry summers
  “Bathtub” style sedimentary basin
    Up to 76 m (250 ft) thick aquifer
  Scott River flows from south to north
    12 major tributary streams
    2 major diversion ditches

## Slide 95: UCD and Affiliated Data Collection and Analysis
Climate Data Analysis
  Build 1944 – 2011 time series
  Spatial trends within Scott Valley
  Water year type analysis
Evapotranspiration
  Estimated
  Surface renewal
  New CIMIS station (225)
Soil moisture and texture sampling
Applied irrigation rates
Well log digitization
Voluntary groundwater monitoring program
SAGBI
Foglia et al., 2013a: http://groundwater.ucdavis.edu/files/165395.pdf

## Slide 96: UCD and Affiliated Data Collection and Analysis (cont.)
Pumping test analysis
  Physical hydraulic properties of aquifer
Evapotranspiration
  Estimated
  Surface renewal
  New CIMIS station (225)
Soil moisture and texture sampling
Applied irrigation rates
Well log digitization
Voluntary groundwater monitoring program
SAGBI

## Slide 97: UCD and Affiliated Data Collection and Analysis (cont.)
Pumping test analysis
  Physical hydraulic properties of aquifer
Evapotranspiration
  Estimated
  Surface renewal
  New CIMIS station (225)
Soil moisture and texture sampling
Applied irrigation rates
Well log digitization
Voluntary groundwater monitoring program
SAGBI
UC Davis, 2016: Voluntary Private Water Level Monitoring Program 2006-2016, http://groundwater.ucdavis.edu/files/153816.pdf

## Slide 98: UCD and Affiliated Data Collection and Analysis (cont.)
Pumping test analysis
  Physical hydraulic properties of aquifer
Evapotranspiration
  Estimated
  Surface renewal
  New CIMIS station (225)
Soil moisture and texture sampling
Applied irrigation rates
Well log digitization
Voluntary groundwater monitoring program
SAGBI
https://casoilresource.lawr.ucdavis.edu/sagbi/

## Slide 99: UCD and Affiliated Data Collection and Analysis (cont.)
Stream temperature observations (DTS)
Chart: Temperature (Deg C)
3.2 ft deep stratified pool
Hines & Harter, UC Davis, draft manuscript

## Slide 100: UCD and Affiliated Data Collection and Analysis (cont.)
Stream temperature observations (DTS)
Agricultural practices survey
  Landuse and irrigation type map updates
Foglia et al., 2013a: http://groundwater.ucdavis.edu/files/165395.pdf

## Slide 101: UCD and Affiliated Data Collection and Analysis (cont.)
Stream temperature observations (DTS)
Agricultural practices survey
  Landuse and irrigation type map updates
Validation of DWR’s Irrigation Demand Calculator (IDC)
http://baydeltaoffice.water.ca.gov/modeling/hydrology/IDC/index_IDC.cfm

## Slide 102: Upper Watershed Model
Regression model
Foglia et al. (2013)

## Slide 103: MODFLOW Model Sensitivity Analysis
Assume simple “black box” model with only 3 parameters
P1
P2
P3
=
+
+

## Slide 104: MODFLOW Model Sensitivity Analysis
P1
P2
P3
=
+
+
=
+
+
=
+
+
=
+
+
Not Sensitive
Sensitive
Not Sensitive

## Slide 105: MODFLOW Model Sensitivity Analysis
Find model parameters that have greatest influence on model results
35 model parameters identified
  Hydraulic conductivity
  Aquifer storage
  Streambed characteristics
  Mountain front recharge
  Ditch seepage
  Recharge scaling factors
Performed 5 different sensitivity analyses
  Different starting values
  Account for model non-linearity
Aquifer Property Zones

## Slide 106: MODFLOW Model Sensitivity Analysis
Find model parameters that have greatest influence on model results
35 model parameters identified
  Hydraulic conductivity
  Aquifer storage
  Streambed characteristics
  Mountain front recharge
  Ditch seepage
  Recharge scaling factors
Performed 5 different sensitivity analyses
  Different starting values
  Account for model non-linearity
Aquifer Property Zones

## Slide 107: MODFLOW Model Sensitivity Analysis
Find model parameters that have greatest influence on model results
35 model parameters identified
  Hydraulic conductivity
  Aquifer storage
  Streambed characteristics
  Mountain front recharge
  Ditch seepage
  Recharge scaling factors
Performed 5 different sensitivity analyses
  Different starting values
  Account for model non-linearity
Aquifer Property Zones

## Slide 108: MODFLOW Model Sensitivity Analysis
6 parameters consistently most sensitive

## Slide 109: MODFLOW Model Calibration
Adjust 6 parameters to minimize difference between observed and simulated values
  Streamflow (at USGS gauge) – 1385 observations
  Groundwater elevations – 2197 observations

## Slide 110: MODFLOW Model Calibration
Despite large number of observations of different types, there is still a problem of non-uniqueness during calibration

## Slide 111: Soil-Water Budget Model
Calculates daily water fluxes at field-scale
Input data (text files)
  Landuse
  Soil properties
  Irrigation type
  Water source
  Potential ET
  Crop Coefficient (Kc)
  Rooting depth
  Precipitation
  Streamflow
Windows executable (.exe)

## Slide 112: Soil-Water Budget Model
Calculates daily water fluxes at field-scale
Input data (text files)
  Landuse
  Soil properties
  Irrigation type
  Water source
  Potential ET
  Crop Coefficient (Kc)
  Rooting depth
  Precipitation
  Streamflow
Windows executable (.exe)

## Slide 113: Soil-Water Budget Model
Calculates daily water fluxes at field-scale
Input data (text files)
  Landuse
  Soil properties
  Irrigation type
  Water source
  Potential ET
  Crop Coefficient (Kc)
  Rooting depth
  Precipitation
  Streamflow
Windows executable (.exe)

## Slide 114: Soil-Water Budget Model Timing
Alfalfa Irrigation
(March 25 – August 31)
Grain Irrigation
(March 15 – July 18)
Pasture Irrigation
(April 15 – October 15)
Alfalfa ET (Constant Kc)
(March 1 – Nov 15)
Grain ET (Variable Kc)
(March 15 – July 18)
Pasture ET (Constant Kc)
(April 15 – October 15)
Kc
Crop Coefficient
Evapotranspiration
Potential ET * Crop Coefficient

## Slide 115: Soil-Water Budget Model - Example
Precipitation
Field Capacity
Maximum Allowable Depletion (0.55*FC)
Groundwater Recharge
Soil Water Content

## Slide 116: Soil-Water Budget Model - Example
Field Capacity
Maximum Allowable Depletion (0.55*FC)
Evapotranspiration = Potential ET * Crop Coefficient
ETc = ETpot*Kc
Irrigation = ETc / Irrigation Efficiency
Calculated each day for each individual field

## Slide 117: Soil-Water Budget Model Output
Daily outputs for each field
  Potential ET
  Actual ET (water limited)
  Total irrigation
  Applied surface-water
  Applied groundwater
  Groundwater recharge
  Soil water content
Groundwater recharge and pumping are averaged to monthly values for MODFLOW model

## Slide 118: Soil-Water Budget Model Output
Daily outputs for each field
  Potential ET
  Actual ET (water limited)
  Total irrigation
  Applied surface-water
  Applied groundwater
  Groundwater recharge
  Soil water content
Groundwater recharge and pumping are averaged to monthly values for MODFLOW model

## Slide 119: Landscape Water Budget

## Slide 120: Landscape Water Budget

## Slide 121: Soil Water Budget Model: Sensitivity Analysis

## Slide 122: Landscape Water Budget

## Slide 123: MODFLOW Model
Pink + Yellow = Layer 1
Yellow = Layer 2
Model Domain
Elevation
  LIDAR (~cm)
  DEM (10 m)
  Averaged to 100 x 100 m
Streambed Elevations
  Scott River thalweg from LIDAR

## Slide 124: MODFLOW Model
Model Domain
Elevation
  LIDAR (~cm)
  DEM (10 m)
  Averaged to 100 x 100 m
Streambed Elevations
  Scott River thalweg from LIDAR

## Slide 125: MODFLOW Model
Model Domain
Elevation
  LIDAR (~cm)
  DEM (10 m)
  Averaged to 100 x 100 m
Streambed Elevations
  Thalweg from LIDAR (where available)
Chart: Scott River Elevation
Vertical Exaggeration = 300x

## Slide 126: MODFLOW Model
Daily time steps with monthly stress periods
  Boundary conditions vary month to month, but not daily; at land parcel scale (fields, canals, streams)
100m lateral discretizatin (relatively high resolution)
Streamflow routing package (SFR) used to simulate Scott River and tributaries
  More sophisticated representation of GW-SW interactions
Oct 1, 1990 – Sep 30, 2011 simulation period

## Slide 127: MODFLOW Model
Daily time steps with monthly stress periods
  Boundary conditions vary month to month, but not daily; at land parcel scale (fields, canals, streams)
100m lateral discretization (relatively high resolution)
Streamflow routing package (SFR) used to simulate Scott River and tributaries
  More sophisticated representation of GW-SW interactions
Oct 1, 1990 – Sep 30, 2011 simulation period

## Slide 128: MODFLOW Model
Daily time steps with monthly stress periods
  Boundary conditions vary month to month, but not daily; at land parcel scale (fields, canals, streams)
100m lateral discretizatin (relatively high resolution)
Streamflow routing package (SFR) used to simulate Scott River and tributaries
  More sophisticated representation of GW-SW interactions
Oct 1, 1990 – Sep 30, 2011 simulation period

## Slide 129: MODFLOW Model
Daily time steps with monthly stress periods
  Boundary conditions don’t vary within a month (but specific for each field, tributary, canal, etc.)
100m lateral discretization (relatively high resolution)
Streamflow routing package (SFR) used to simulate Scott River and tributaries
  More sophisticated representation of GW-SW interactions
Oct 1, 1990 – Sep 30, 2011 simulation period
Specify for each node
  Elevation
  Reach length
  Reach width
  Bed hydraulic conductivity
  Bed thickness
  Bed slope

## Slide 130: MODFLOW Model
Daily time steps with monthly stress periods
  Boundary conditions vary month to month, but not daily; at land parcel scale (fields, canals, streams)
100m lateral discretizatin (relatively high resolution)
Streamflow routing package (SFR) used to simulate Scott River and tributaries
  More sophisticated representation of GW-SW interactions
Oct 1, 1990 – Sep 30, 2011 simulation period
Ditches and Mountain Front Recharge

## Slide 131: MODFLOW Model
Daily time steps with monthly stress periods
  Boundary conditions vary month to month, but not daily; at land parcel scale (fields, canals, streams)
100m lateral discretizatin (relatively high resolution)
Streamflow routing package (SFR) used to simulate Scott River and tributaries
  More sophisticated representation of GW-SW interactions
Oct 1, 1990 – Sep 30, 2011 simulation period

## Slide 132: MODFLOW Model
Windows executable (.exe) with text file inputs
  MODFLOW OWHM using Newton (NWT) Solver
    Allows for rewetting of cells that go dry along basin margin
  Specify name (.nam) file that calls the following input files:
  ~45 to 60 min runtime
  Binary and text output files
    Binary files need to be translated before they can be used

## Slide 133: MODFLOW Model
Windows executable (.exe) with text file inputs
  MODFLOW OWHM using Newton (NWT) Solver
    Allows for rewetting of cells that go dry along basin margin
  Specify name (.nam) file that calls the following input files:
  ~45 to 60 min runtime
  Binary and text output files
    Binary files need to be translated before they can be used
.bas | .dis | .upw | .zone
.hob | .pvl | .sfr | .gag
.wel | .ets | .rch | .oc
 | .mult | .nwt | 

## Slide 134: MODFLOW Model
Windows executable (.exe) with text file inputs
  MODFLOW OWHM using Newton (NWT) Solver
    Allows for rewetting of cells that go dry along basin margin
  Specify name (.nam) file that calls the following input files:
  ~45 to 60 min runtime
  Binary and text output files
    Binary files need to be translated before they can be used
.bas | .dis | .upw | .zone
.hob | .pvl | .sfr | .gag
.wel | .ets | .rch | .oc
 | .mult | .nwt | 

## Slide 135: MODFLOW Model
Windows executable (.exe) with text file inputs
  MODFLOW OWHM using Newton (NWT) Solver
    Allows for rewetting of cells that go dry along basin margin
  Specify name (.nam) file that calls the following input files:
  ~45 to 60 min runtime
  Binary and text output files
    Binary files need to be translated before they can be used
.bas | .dis | .upw | .zone
.hob | .pvl | .sfr | .gag
.wel | .ets | .rch | .oc
 | .mult | .nwt | 

## Slide 136: Relative Stream Depletion from Well Pumping (or: Relative Stream Repletion from Intentional Recharge)
Bredehoeft, 2010
Infinite, confined, uniform aquifer, fully penetrated by the stream.
Q
K, S
distance, a
q
thickness, b

## Slide 137: Soil water balance and saturated/unsaturated flow model
Thornthwaite-Mather model (root zone, 0-2ft)
AWC = available water content
Soil water balance
R = Deep percolation (in)
I = applied winter water (in) at time t,
P = precipitation (in),
ET = evapotranspiration (in),
ΔS = change in soil storage (in) (dependent on AWC)
Q = surface runoff (in).
1D saturated/unsaturated flow model (transmission zone, 2-5ft)
θt = volumetric water content (volume fraction) at time t, θs = volumetric water content at field capacity
θd = volumetric water content at the wilting point (volume fraction), κ is a constant (positive), Ksat is the saturated hydraulic conductivity, and is the time step.
Dahlke et al. 2017, submitted
Notes: Use Thornthwaite-Mather soil water balance model to estimate deep percolation and losses to evapotranspiration and soil storage
Use 1D van Genuchten-Mualem model to estimate recharge into deeper soil

## Slide 138: Deep percolation estimates – Scott Valley
Water table rose up to 6 ft in response to winter recharge
θs = 0.57, θd = 0.1
θs = 0.46, θd = 0.08
AWC (SSURGO) = 4.9”
AWC (1D model) = 15–18.5”

## Slide 139: Travel time of water to groundwater table

## Slide 140: Crop yield – both sites
Application of up to 26 ft of water caused no discernible difference in alfalfa yield
Crop response in Davis was impacted by gopher damage
Scott Valley
Davis, CA

## Slide 141: Crop Water Use
ETc = Kc x ETo
Crop Evapotranspiration (ETc) is calculated by multiplying the reference crop evapotranspiration, ETo, by a crop coefficient, Kc:

## Slide 142
Region | Site | Year | Age Of alfalfa | Seasonal ET (inches) | Reference ET (inches)
Imperial Valley | LM1 LM2 LM2 GR EL WA | 2007 2008 2009 2010 2010 2010 | 3 2 3 2 2 2 | 55.8 66.0 55.6 63.5 59.8 65.8 | 73.2 73.3 67.9 73.2 70.0 70.0
San Joaquin Valley | KC KC | 2007 2008 | 2 3 | 56.6 59.4 | 57.0 59.3
Sacramento Valley | CH1 CH2 CH2 CH2 EE EW | 2005 2006 2007 2008 2010 2010 | 3 2 3 4 3 4 | 49.4 54.8 55.0 50.4 46.3 42.5 | 63.6 55.9 58.0 59.4 48.8 48.8
Scott Valley/Shasta Valley | EN EN EN FI SH AP FI FA | 2007 2008 2009 2009 2009 2010 2010 2010 | 2 3 4 5 4 5 2 6 | 39.6 32.8 33.8 36.1 38.8 37.3 34.7 38.8 | 44.0 42.6 40.4 37.4 40.4 37.4 37.4 41.1
Tulelake | TU TU | 2007 2008 | 4 5 | 39.0 34.3 | 40.5 36.5
Ave. 37 in.

## Slide 143: So…How is Applied Water Calculated? And, how much water should growers apply to alfalfa (and what to assume in model)
Item | Explanation | Amount
Alfalfa ET | (March 15 – October 1) | 40 in.
Soil moisture contribution | 4 ft. rooting depth x 2 in. avail/ft. | 8 in.

## Slide 144: So…How is Applied Water Calculated? And, how much water should growers apply to alfalfa (and what to assume in model)
Item | Explanation | Amount
Alfalfa ET | (March 15 – October 1) | 40 in.
Soil moisture contribution | 4 ft. rooting depth x 2 in. avail/ft. | 8 in.
In-season rainfall | 6 in. (effective rainfall?) | 6 in.

## Slide 145: So…How is Applied Water Calculated? And, how much water should growers apply to alfalfa (and what to assume in model)
Item | Explanation | Amount
Alfalfa ET | (March 15 – October 1) | 40 in.
Soil moisture contribution | 4 ft. rooting depth x 2 in. avail/ft. | 8 in.
In-season rainfall | 6 in. (effective rainfall?) | 6 in.
Net irrigation | Amount needed to satisfy ET | 26 in.

## Slide 146: Application Efficiencies for Different Irrigation Systems (Canessa et al. 2011)
Irrigation System | Application Low | Efficiencies Mean | (%) High
Surface Irrigation |  |  | 
Wild Flood | 50 | 68 | 86
Border | 62 | 73 | 83
Basin | 72 | 83 | 93
Furrow | 60 | 73 | 85
Sprinkler |  |  | 
Permanent | 70 | 78 | 85
Hand-Move | 60 | 70 | 80
Linear-Move | 73 | 82 | 90
Side-Roll | 60 | 70 | 80
Hose-Pull | 70 | 73 | 75
Center-Pivot | 70 | 80 | 90
Drip |  |  | 
Above ground | 77 | 86 | 95
Buried drip | 77 | 86 | 95
Flood Irrigation 70%; Wheel-line 75%; Center Pivot 90%;

## Slide 147: So…How is Applied Water Calculated? And, how much water should growers apply to alfalfa (and what to assume in model)
Item | Explanation | Amount
Alfalfa ET | (March 15 – October 1) | 40 in.
Soil moisture contribution | 4 ft. rooting depth x 2 in. avail/ft. | 8 in.
In-season rainfall | 6 in. (effective rainfall?) | 6 in.
Net irrigation | Amount needed to satisfy ET | 26 in.
Gross irrigation | 26 in. ÷ 0.78 (applic. effic.) | 33.3 in

## Slide 148
Eight commercial alfalfa fields
(4 center pivot & 4 wheel-line)
  Surface renewal instruments in 3 of the 8 fields
  Temporary CIMIS station in an irrigated pasture
  Gravimetric soil moisture content determined April-March and early October down to 8 feet
  Watermark sensors at 1-foot increments down to 8 feet (2 locations per field)
  Permanently installed flow meters some systems
  Nozzle output on wheel-line sprinklers
  Tipping rain gauge at each site
  Yield measurements at each cutting
ET
Soil
Irrig.

## Slide 150
Irrigation Interval Around Cuttings Wheel-Line Fields
2012 & 2013
 | Irrigation Interval Before – After 1st Cut (days) | Irrigation Interval Before – After 2nd Cut (days)
Grower 1 | 30 | 24
Grower 2 | 52 | 29
Grower 3 | 25 | 22
Grower 4 | 41 | 19
Grower 1 | 38 | 30
Grower 2 | 48 | 41
Grower 3 | 42 | 24
Grower 4 | 34 | 33
Mean | 39 | 28

## Slide 151
Irrigation Interval Around Cuttings Center Pivot Fields
2012 & 2013
 | Irrigation Interval Before – After 1st Cut (days) | Irrigation Interval Before – After 2nd Cut (days) | Irrigation Interval Before – After 3rd Cut (days)
Grower 1 | -- | 25 | --
Grower 2 | 29 | 20 | --
Grower 3 | 29 | 29 | --
Grower 1 | 35 | 14 | 18
Grower 2 | 24 | 18 | 16
Grower 3 | 26 | 17 | --
Grower 4 | 42 | 17 | --
Mean | 31 | 19 | 17

## Slide 152
Chart: Soil Moisture Tension (centibars)
| 41026 | 41033 | 41039 | 41045 | 41052 | 41059 | 41066 | 41073 | 41080 | 41087 | 41095 | 41101 | 41108 | 41116 | 41123 | 41130 | 41137 | 41144 | 41151 | 41158 | 41165 | 41172 | 41179
1 ft. | 16 | 28.5 | 8.5 | 23 | 58 | 83.5 | 120.5 | 3 | 10 | 22.5 | 19.5 | 18.5 | 63 | 147 | 92.5 | 3 | 3 | 26 | 47.5 | 78 | 145.5 | 213 | 219
2 ft. | 2.5 | 7.5 | 4 | 5 | 14.5 | 23 | 38.5 | 44 | 2 | 12.5 | 4.5 | 15 | 43 | 122 | 125 | 1.5 | 1 | 13.5 | 28.5 | 58.5 | 133.5 | 144.5 | 171
3 ft. | 4 | 6.5 | 4.5 | 5.5 | 7 | 14.5 | 19 | 25.5 | 27.5 | 30.5 | 29 | 33.5 | 49.5 | 115.5 | 121.5 | 21 | 11 | 11 | 24 | 47.5 | 124 | 137.5 | 170
4 ft. | 2 | 3 | 4 | 4.5 | 6.5 | 11 | 17 | 21.5 | 24.5 | 27 | 28 | 30.5 | 37.5 | 60 | 91 | 79.5 | 63 | 30.5 | 25 | 45.5 | 111 | 115 | 122.5
5 ft. | 2 | 1.5 | 2.5 | 3 | 7.5 | 14.5 | 18.5 | 21.5 | 23 | 25 | 27 | 29 | 35.5 | 51.5 | 63 | 55 | 54.5 | 56 | 59 | 67.5 | 89 | 118.5 | 125.5
6 ft. | 2.5 | 2 | 3 | 4 | 6.5 | 14 | 16.5 | 18.5 | 21 | 23 | 25.5 | 28 | 30.5 | 39 | 43 | 44 | 45 | 46.5 | 48 | 52.5 | 60 | 72.5 | 87.5
7 ft. | 3 | 2 | 5.5 | 8 | 13.5 | 16 | 19 | 25 | 22 | 23 | 25 | 27 | 30 | 37 | 41.5 | 43 | 44 | 45 | 46.5 | 48.5 | 56 | 67 | 80
8 ft. | 10 | 10.5 | 12.5 | 15.5 | 17.5 | 20 | 21.5 | 22 | 23 | 24 | 25.5 | 26.5 | 29 | 35 | 39 | 39.5 | 40.5 | 41 | 42 | 44 | 49 | 56 | 65.5
Seasonal Soil Moisture Levels
Scott Valley, 2012 (Grower A)

## Slide 153
Chart: Soil Moisture (centibars)
| 41026 | 41033 | 41039 | 41045 | 41052 | 41059 | 41066 | 41073 | 41080 | 41087 | 41095 | 41101 | 41108 | 41116 | 41123 | 41130 | 41137 | 41144 | 41151 | 41158 | 41165 | 41172 | 41179
1 ft. | 19.5 | 31.5 | 44.5 | 15.5 | 36 | 32.5 | 14 | 57 | 106.5 | 189 | 97 | 114 | 4.5 | 51 | 26 | 16 | 7 | 22 | 16 | 74 | 107.5 | 190.5 | 215
2 ft. | 14 | 22.5 | 32.5 | 58.5 | 36.5 | 76.5 | 67.5 | 112.5 | 190 | 216 | 109.5 | 137 | 147 | 148 | 188.5 | 77.5 | 75.5 | 15 | 25 | 53.5 | 79.5 | 137.5 | 219
3 ft. | 14.5 | 20 | 28 | 47.5 | 70 | 112.5 | 145 | 178 | 212 | 219 | 219 | 219 | 219 | 219 | 219 | 117.5 | 131 | 127.5 | 137.5 | 150 | 162.5 | 190 | 219
4 ft. | 29.5 | 33 | 38 | 51.5 | 65 | 87 | 105.5 | 134 | 174.5 | 203.5 | 211 | 212.5 | 211.5 | 213.5 | 211 | 206.5 | 207.5 | 207.5 | 208 | 210 | 218.5 | 219 | 219
5 ft. | 68.5 | 77.5 | 83.5 | 79 | 87.5 | 102.5 | 105 | 121.5 | 147.5 | 173.5 | 199.5 | 205 | 198.5 | 206.5 | 207 | 198 | 195 | 188.5 | 188.5 | 189 | 194.5 | 200.5 | 219
6 ft. | 39.5 | 42 | 44.5 | 71.5 | 82 | 94 | 102 | 113.5 | 133 | 152.5 | 170.5 | 173.5 | 174.5 | 175 | 170 | 166 | 164.5 | 160.5 | 162 | 167.5 | 176.5 | 202 | 198.5
7 ft. | 23.5 | 23 | 23 | 24.5 | 25 | 26 | 27 | 30 | 38.5 | 43 | 50 | 56.5 | 65 | 69 | 79 | 68.5 | 67 | 61.5 | 59.5 | 58.5 | 62 | 78 | 98.5
8 ft. | 17 | 16.5 | 16 | 16.5 | 17 | 17.5 | 16.5 | 17 | 17.5 | 17 | 18 | 18.5 | 19 | 19.5 | 20 | 20 | 20 | 20 | 20.5 | 20.5 | 21.5 | 24 | 28.5
Seasonal Soil Moisture Levels
Scott Valley, 2012 (Grower G)

## Slide 154: Application Efficiency
How well an irrigation system performs to get water to plant roots
Portion of the total water volume delivered to the field that is stored in the root zone that is available to meet crop evapotranspiration (ET)
Losses: deep percolation and runoff
So if under-irrigating…

## Slide 155: Conclusions
Grower application rates approximately 1/3 less than assumed values
Seasonal Kc 0.92 rather than 0.95 – 0.99 (0.90 likely representation of Valley overall)
Many growers under irrigating so not refilling profile and little to no in-season deep percolation
Long intervals between irrigations around cuttings
When under-irrigating application efficiency approaches 100%
Therefore, when estimating water application rates, cannot use ET value and divide by assumed application efficiency for given irrigation system